## Slide 1: Fire Engine Driving Operations
Unit 3A – Driving Policy and Procedures
Version: January 2023

## Slide 2: Objectives
Discuss agency policies and regulations related to driving fire engines.
Discuss and interpret duty-day limitations.
Identify the components of a risk assessment (RA).

## Slide 3: Agency Policies and Regulations
Notes: Policies are set in place because of what has happened before. For safety.

## Slide 4: Drug-Free Work Place
Executive Order 12564
Fit For Duty
Interagency Standards for Fire and Fire Aviation Operations
Notes: Fit For Duty

## Slide 5: Fire Vehicle Operation Standards

## Slide 6: State Traffic Regulations

## Slide 7: State Traffic Regulations

## Slide 8: Lights
Notes: Red Lights and Sirens Policy may differ from unit to unit. Ensure you know your units policy and the policy for requirements when off unit.

## Slide 9: General Driving Policy
Valid state driver’s license/entry-level driver training (ELDT)
Government Motor Vehicle Operator’s Identification Card (BLM & BIA policies)
Defensive driver training
BL-300/RT-301
Seat belts
Physical Fitness Inquiry for Motor Vehicle Operators (BLM policy)
Notes: Government Motor Vehicle Operator’s Identification Card:
BLM – BLM Form 1112-11, Motor Vehicle/Special Equipment Authorization
BIA – GSA Form 3607, Motor Vehicle Operator’s License and Driving Record (annually)

## Slide 10: Driving Limitations
CDL for ENOPs operating vehicles in excess of 26,000 GVW
DOT exemptions for wildland fire
Notes: Share ELDT information with class _ Entry Level Driver Training Requirements

## Slide 11: Incident Operations Driving
No driver will drive more than 10 hours (behind the wheel) within any duty day.
Multiple drivers in a single vehicle may drive up to the duty-day limitation provided no driver exceeds the individual driving (behind the wheel) time limitation of 10 hours.
Driving hours are from 0500-2200 hours.
To manage fatigue, every effort should be made to avoid off-unit (excluding IA response) mobilization and demobilization travel between 2200-0500 hours.
Notes: 25 IAM Chapter 4 is the official BIA driving policy, updated in April 2020. This sets the duty day limitations for one driver at 8 hours. This is also in the 2022 Red Book.

## Slide 12: Incident Operations Driving
A driver shall drive only if he/she has had at least eight (8) consecutive hours off duty before beginning a shift. Exception to the minimum off-duty hour requirement is allowed when essential to:
  Accomplish immediate and critical suppression objectives.
  Address immediate and critical firefighter or public safety issues.

## Slide 13: Work/Rest Guidelines
Documentation is required for shifts in excess of 16 hours.
Minimum 2:1 work-to-rest ratio (for every two hours of work or travel, provide one hour of sleep and/or rest)

## Slide 14: Work/Rest Driving Scenarios

## Slide 15: Scenario 1
You (the ENOP with a CDL) and a module member (non-CDL driver) are traveling to another state in a Type 4 engine. The trip length is estimated at 26 hours.
  How many days will it take to reach your destination?

## Slide 16: Scenario 1 - Answer
Three days
“No driver will drive more than 10 hours (behind the wheel) within any duty day.”
The non-CDL driver is not allowed to drive the engine.

## Slide 17: Scenario 2
You (the ENOP with a CDL) and a module member (non-CDL driver) are traveling to another state in a Type 6 engine. The trip length is estimated at 26 hours.
  How many days will it take to reach your destination?

## Slide 18: Scenario 2 - Answer
Two days
“Multiple drivers in a single vehicle may drive up to the duty-day limitation provided no driver exceeds the individual driving (behind the wheel) time limitation of 10 hours.”
The non-CDL driver is allowed to drive the engine, but both drivers are subject to the 16-hour duty day.

## Slide 19: Scenario 3
While on assignment on a 200,000-acre fire and working 12-hour shifts, the division group supervisor asks your crew to work an extra 8-hour shift to monitor the line.
  Is this something your crew can do?

## Slide 20: Scenario 3 - Answer
No. This will exceed the 2:1 work-to-rest ratio.
  However, the Incident Commander could write a justification authorizing the action.

## Slide 21: Driver Walk-around
A driver walk-around will be done every time the engine is moved.

## Slide 22: Hazardous Materials

## Slide 23: Safety and the RA

## Slide 24: What is a Risk Assessment?
A risk assessment (RA) is a technique that focuses on job tasks as a way to identify hazards before they occur. It focuses on the relationship between the worker, the task, the tools, and the work environment. Ideally, after you identify uncontrolled hazards, you will take steps to eliminate or reduce them to an acceptable risk level.

## Slide 25: Why Complete a Risk assessment?
A completed RA is required for:
  Jobs or work practices that have potential hazards.
  New, non-routine, or hazardous tasks to be performed where potential hazards exist.
  Jobs that may require the employee to use non‑standard personal protective equipment (PPE).
  Changes in equipment, work environment, conditions, policies, or materials.
    Interagency Standards for Fire and Fire Aviation Operations

## Slide 26: Why do a Risk Assessment? (Continued)
  Supervisors and appropriate line managers must ensure that established JHAs are reviewed and signed prior to any non-routine task or at the beginning of the fire season.
  BLM – A risk assessment (in lieu of JHA) must be completed for all non-suppression work practices/projects that have potential hazards.”
    Interagency Standards for Fire and Fire Aviation Operations
    FOR BIA
    A completed JHA/RA is required for:
    • Jobs or work practices that have potential hazards.
    Interagency Standards for Fire and Fire Aviation Operations

## Slide 27: Tailgate Safety Session
Notes: BIA utilizes tailgate safety sessions as a component of discussing the risk assessment and identifying mitigations for hazards.

## Slide 28: Objectives
Discuss agency policies and regulations related to driving fire engines.
Discuss and interpret duty-day limitations.
Identify the components of a risk assessment (RA).