## Slide 1: Water Handling Operations
Unit 4C - Foam and Foam Proportioning Equipment

## Slide 2: Objectives
Discuss why foam is more effective than plain water when performing wildland fire suppression operations.
Discuss foam safety, including guidelines for handling foam products.
Identify and discuss the advantages and disadvantages of two manual foam proportioning methods used when performing wildland fire suppression operations.

## Slide 3: Objectives
Identify various operational components of the FoamPro® 1600/1601 and Waterous Aquis 1.5.
Demonstrate the ability to set up, run, have foam solution pumped to a nozzle person, and shut down a foam proportioner.

## Slide 11: Safety equipment

## Slide 13: Foam Proportioners

## Slide 14: Manual Foam Proportioners
Operators manually adjust the device to maintain a constant mix ratio when water flow and pressure changes.
  Cannot maintain constant mix ratio over various flow and pressure rates

## Slide 15: Batch Mixing

## Slide 16: Suction-Side Proportioners

## Slide 18: Automatic Foam Proportioner
The automatic foam proportioner makes an adjustment on its own to maintain a constant mix ratio when water flow and pressure changes.
Waterous Aquis™ 1.5
FoamPro® 1601

## Slide 19: Foam Proportioner
s

## Slide 20: Foam Proportioner
Proportional and automatic
Works on discharge side of pump
Class A foam only
Requires water flow and electrical current
No restrictions due to hose length or number of nozzles
No loss of pressure or flow
Accurate at all flow ranges
Resupply foam without interruption

## Slide 21: Operating the Foam Proportioner Major Components
Operator control module
Motor driver box/module
Paddlewheel flowmeter
Foam pump and electric motor
Calibrate/Inject valve
Inline strainer

## Slide 22: Operator Control Module Panel Mounted
Operating instructions
On/Off switch
Injection rate control
  Adjustable from 0.1%-1.0%
Low concentrate (“LOW CONC.”) light

## Slide 23: Motor Driver Box/Module Normal Operation
Circuit breaker switch “Up” for normal operation
Simulated flow switch “Down” for normal operation

## Slide 24: Paddlewheel Flowmeter

## Slide 25: Foam Pump and Electric Motor

## Slide 26: Calibrate/Inject Valve

## Slide 27: Purging Air
Enter “Simulated Flow”
  Switch to “Up” position
  Preprogrammed for 100 gpm
Valve to “Cal/Flush”
Turn panel switch “On”
Run pump until concentrate flows from dump line

## Slide 28: Purging Air Continued
Turn control panel to “Off” position
Return valve to “Inject”
Exit “Simulated Flow” by returning switch to “Down” position

## Slide 29: Inline Strainer

## Slide 30: Foam Injection Check Valve and Injection Port

## Slide 31: Objectives
Discuss why foam is more effective than plain water when performing wildland fire suppression operations.
Discuss foam safety, including guidelines for handling foam products.
Identify and discuss the advantages and disadvantages of two manual foam proportioning methods used when performing wildland fire suppression operations.

## Slide 32: Objectives
Identify various operational components of the FoamPro® 1600/1601 and Waterous Aquis 1.5.
Demonstrate the ability to set up, run, have foam solution pumped to a nozzle person, and shut down a foam proportioner.